Truth Studies in pp→ttH channel
Georgios Billis
Supervisor: Prof. Niki Saoulidou – National and Kapodistrian	University of Athens

---
Outline
- Description of the main method
- Results of the main method
- Goal of the study
- Truth level study of various kinematic and topological distributions
- TMVA invastigation
- Summary – On going work

---
Description of the main method
- The work revolves around the pp→ ttH channel in LHC accelerator (CMS)
- Investigation of the dilepton tt decay

---
Description of the main method
- Main method solves analyticaly the kinematic equations that dictate the former topology.
- Obtain 0,2,4 solutions for the neutrino momenta given the masses of top and W boson.

---
Description of the main method
- Exploiting that the dilepton channel can be completely solved analytically, a model independent method is employed for the reconstruction of the top and W mass.
- Scan the 2D mass plane of t-W and set them as inputs in the kinematic equations.
- Having all the kinematic variables of the topology, the (product) PDF weight can be calculated.
- After the the 2D mass plane scan, the solution with the greatest PDF weight is chosen→ obtain the mass of top and W.

---
Description of the main method
C.K.Koraka – University of Athens

---
Description of the main method
- Extrapolation in the case that a Higgs is also produced.
- Does not affect the method – but increases the combinatorics (4 b jets).

---
Description of the main method
The inputs of the method are now:
- 4 bjets
- 2 leptons
- Missing transverse energy
- Mass of top & W

---
Results of the main method

---
Goal of truth study
- Under certain optimization the maximum PDF weight yields the correct Higgs mass at ~43% of the events.
- Goal is to find a possibly better estimator of the correct tt solution → TMVA
- Several kinematic and topological distributions show discriminating power between the correct and wrong solution.

---
Technical Details
In what follows only truth events have been studied:
1) As “correct” are defined those events that satisfy Δpx=Δpy=Δpz=0 for the neutrino momenta. (Δp_i=generated mom. - solved by method mom.).
2)As “wrong” are defined those that do not satisfy condition (1).

---
Δφ between lepton and all b jets
Positive lepton
Negative lepton
The Δφ distributions show significant discriminating power between the correct and wrong solutions.

---
Δη between lepton and all b jets
Positive lepton
Negative lepton

---
ΔR between lepton and all b jets
Positive lepton
Negative lepton

---
Δφ between 1st and 2nd bjet of Higgs with the rest of b jets
1st b-jet of Higgs
2nd b-jet of Higgs

---
Δη between 1st and 2nd bjet of Higgs with the rest of b jets
1st b-jet of Higgs
2nd b-jet of Higgs

---
ΔR between 1st and 2nd bjet of Higgs with the rest of b jets
1st b-jet of Higgs
2nd b-jet of Higgs

---
Pt asymmetry and Ratio of Higgs jets
(PT1-pT2)/(PT1+pT2)
(pT1/pT2)

---
Energy of the tt system and PDF weights ratio
Energy of the tt system
Ratio = w/w_max
Good discriminative power.